## Slide 1
DIPARTIMENTO DI INGEGNERIA ELETTRICA E TECNOLOGIE DELL’INFORMAZIONE
SCUOLA POLITECNICA E DELLE SCIENZE DI BASE
Field and Service Robotics project
Navigation planning and control of car-like robot
Candidate: Manzoni Antonio
Supervisor: Prof. Fabio Ruggiero
MASTER'S DEGREE IN AUTOMATION ENGINEERING AND ROBOTICS
YUHESEN FR-09 PRO

## Slide 2
2/28
Index
Aim of the project
Kinematic model of car-like robot
Navigation planning
  RRT* with Pseudo-Clothoid curves
  Dijkstra and A* algorithms with Reeds-Sheep curves exploration
Input-Output Linearization control
Simulations and results

## Slide 3
INPUT-OUTPUT LINEARIZATION CONTROL
3/28
Aim of the project
NAVIGATION PLANNING
A smooth path planning algorithm is implemented to determine the trajectory for car-like robots. Three different strategies of path planning are introduced:
RRT* with Pseudo-Clothoid curves
Dijkstra and A* algorithms with Reeds-Shepp Curves
Given the trajectory in the previous point, an Input/Output Linearization control approach is implemented to control the position of car-like robot.

## Slide 4
4/28
Car-like robot: kinematic modeling
Two nonholonomic constraints, one for each wheel (pure rolling constraints)
Using rigid-body constraints
Pfaffian constraint matrix
Kinematic model (rear-wheel driving)
the second kinematic constraint becomes

## Slide 5
5/28
Navigation planning: steps
Path planning (find a path from to with an algorithm)
Obstacle avoidance
Smooth path generation considering the nonholonomic constraints of car-like robots.
From geometric path, create a desired trajectory in terms of to be given as input to the controller

## Slide 6
6/28
Navigation planning: path planning strategies
RRT*
Pseudo-Clothoid
Curves
Goal: obtain a smooth path
Reeds-Shepp Curves
Dijkstra algorithm
A* algorithm
Sampling-based
Search-based

## Slide 7
7/28
Navigation planning: Sampling-based approach (RRT*)
Main loop
Rewiring
Path reconstruction
Random sampling
Finds the closest point to the random point using the Euclidean distance
Computes the new point by steering from the nearest point toward the random point
Checks collisions with obstacles and map boundaries
Finds neighboring nodes within a certain radius and selects the one with minimum cost
Adds the new point to the tree with the minimum-cost node as parent
Examines all neighboring nodes to improve existing paths:
:
Reconnects to the new node
Updates the cost of
Propagates the improvement to all descendants
When a node is sufficiently close to the goal reconstructs the complete path from goal to start by following parents
Updates the best path if it has a lower cost than previous ones
Notes: cost(qmin) = cost(qnearest) + distance(qmin, qnearest)

## Slide 8
8/28
Navigation planning: Pseudo-clothoid curves
To obtain a smooth expansion of the tree, a modified version of the clothoid curves with a variable turning radius has been made.
Variable turning radius that decreases as angle increases:
Arc center calculation using heading direction :
Angle calculation for each curve point:
Coordinates computation without numerical integration:
: initial radius of the curve
: rate of change of the angle
covered angular distance
: current heading angle
: distance along the curve
Parameters

## Slide 9
9/28
Navigation planning: Bézier termination
Problem: radius might become too small at curve end, creating infeasible curvature
Solution: terminate with a cubic Bézier curve
Cubic Bézier curve equation:
Control points definition:
start point (coincides with last point of pseudo-clothoid)
intermediate control points shaping curve trajectory
target point (the sampled random point)

## Slide 10
10/28
Navigation planning: Search-based approaches (A*, Dijkstra)
Exploration loop
Path finding
Connection phase
Creates grid representation using Reeds-Shepp curves as motion primitives
Employs a queue-based exploration system, where the queue contains the nodes to explore, initialized with the start point:
  Dijkstra: simply selects the first node of the queue (FIFO)
  A*: sorts the queue by the total cost
Generates occupancy matrix tracking obstacles and visited nodes
Builds network of feasible physical connections
Converts exploration results to adjacency matrix (graphs' domain). Adjacency matrix contains node connections and distances
Applies graph search algorithms on network to find the shortest/best path:
  Dijkstra: finds shortest path by minimizing distance
  A*: finds best path by minimizing
Works on validated connections from exploration phase
Determines best sequence of movements through network
Connects the start point to the goal point following the path retrieved by the previous phase
Ensures that the continuous path meets the non-holonomic constraints of the robot
(Optional): Implements a smooth forced connection with a spline curve in the last part of the path to reach exactly the goal. This must perform also a final validation for obstacle avoidance
Notes: Update of the queue and the occupancy matrix as exploration progresses.

## Slide 11
11/28
Navigation planning: Reeds-Shepp curves
Circular arcs of varying lengths traversed with velocities:
The radius of these circular arcs is determined by
Linear segments of varying lengths traversed with velocities:
No cusps because the movement is always forward.
Dubins Curves
The curves are designed to satisfy the kinematic constraints of the robot, considering only certain Navigation primitives ( and for circular arcs and for linear segments).
Velocity limits:

## Slide 12
12/28
Navigation planning: path finding (Dijkstra)
Graph setup
Core algorithm
Works with the adjacency matrix representing valid connections
Creates a distance array initialized to infinity for all nodes
Sets distance to zero for the starting node
Maintains a set of unvisited nodes containing all graph nodes
Iteratively selects unvisited node with minimum distance
For each neighbor connected to current node:
    Calculates potential new distance via current node
    If new distance is shorter than currently recorded distance:
        Updates the distance value
        Records current node as the neighbor's predecessor
    Marks current node as visited
    Continues until all nodes are visited or goal is reached

## Slide 13
13/28
Navigation planning: path finding (A*)
Graph setup
Core algorithm
Works with the adjacency matrix representing valid connections
Initializes the total cost array for each node:
Where:
  : Distance from start node (initially infinity except 0 for start)
  : Heuristic estimate to goal using Euclidean or Manhattan distance
Creates priority queue containing all nodes, ordered by f-cost
Iteratively selects unvisited node with minimum f-cost
For each neighbor connected to current node:
    Calculates potential new g-cost via current node
    If new g-cost is better than current g-cost:
        Updates g-cost value
        Recalculates f-cost as g-cost + h-cost
        Updates predecessor reference for path reconstruction
    Marks current node as visited
    Terminates when goal is reached or no more nodes to process

## Slide 14
14/28
Navigation planning: trajectory
Create desired trajectory in terms of to be given as
input to the controller
Geometric path
Adding time law
From the geometric path is possible to retrieve the Cartesian coordinates () of the points, which represent the robot position in the 2D space without specifying a timing law.
1
2
The time law 𝑠(𝑡) is defined as a function that maps time 𝑡 to the arc length 𝑠 of the geometric path. A 5th-order polynomial for RRT* and a piecewise cubic Hermite polynomial for A* and Dijkstra have been chosen to fulfill this task.
4
3
Interpolation
The coordinates mapped in terms of time now had to be interpolated. For each instant in the new grid, the corresponding value of s(t) is calculated and the coordinates (x(t), y(t)) are determined
by cubic spline interpolation, subsequently applying a smoothing function to ensure continuity.
TRAJECTORY = PATH + TIMING LAW

## Slide 15
15/28
Input-Output Linearization control
The output choice for the trajectory tracking task is:
System output is redefined as:
Heading velocity and steering angle velocity:
Controller
The time derivatives of these outputs (substituting the kinematic model of the car-like robot) :
 coordinates of midpoint of the axle of rear wheels
 coordinates of the point P
Since , we can set:

## Slide 16
16/28
Input-Output Linearization control
Desired trajectory
Outputs
Desired outputs
Velocities
Virtual control inputs
Current states
Current states

## Slide 17
17/28
Input-Output Linearization control
RRT*
Dijkstra - A*

## Slide 18
18/28
Simulations and Results: RRT* approach
RRT* path finding
Desired trajectory in MATLAB
Desired trajectory in SIMULINK
Performed trajectory in SIMULINK

## Slide 19
19/28
Simulations and Results: RRT* approach
Error of
Error of
Error of
Error of

## Slide 20
20/28
Simulations and Results: RRT* approach
Heading velocity and steering angle velocity in MATLAB
Heading velocity and steering angle velocity in SIMULINK

## Slide 21
21/28
Simulations and Results: Dijkstra approach
Dijkstra path finding
Desired trajectory in MATLAB
Desired trajectory in SIMULINK
Performed trajectory in SIMULINK
Smooth forced connection

## Slide 22
22/28
Simulations and Results: Dijkstra approach
Error of
Error of
Error of
Error of

## Slide 23
23/28
Simulations and Results: Dijkstra approach
Heading velocity and steering angle velocity in MATLAB
Heading velocity and steering angle velocity in SIMULINK

## Slide 24
24/28
Simulations and Results: A* (Manhattan) approach
Desired trajectory in MATLAB
Desired trajectory in SIMULINK
Performed trajectory in SIMULINK
Smooth forced connection
A* path finding

## Slide 25
25/28
Simulations and Results: A* (Manhattan) approach
Error of
Error of
Error of
Error of

## Slide 26
26/28
Simulations and Results: A* (Manhattan) approach
Heading velocity and steering angle velocity in SIMULINK
Heading velocity and steering angle velocity in MATLAB

## Slide 27
27/28
Simulations and Results: Comparing A* and Dijkstra
Nodes comparison
Exploration ratio

## Slide 28
28/28
Simulations and Results: Final considerations
Aspect | Sampling-based (RRT)* | Search-based (Dijkstra, A*)
Complexity | Well-suited for high-dimensional spaces and complex environments | May struggle with "curse of dimensionality" in high-dimensional spaces
Optimality | Converges to optimal solutions as the number of iteration increases | Designed to find optimal solutions within the discretized space
Convergence | Balances exploration with optimization, converging to optimality over time | May require significant computation time in complex environments
Hybrid solutions that combines the strengths of both the approaches have been developed :
Use sampling-based planners for initial rapid exploration
Switch to search-based approaches near the goal region
This combination balances efficient space exploration with optimality guarantees

## Slide 29
29/28
Thank you for your attention !!